## Slide 1: Adaptive Staircase Measurement of Hand Proprioception
Hoseini et al., 2015
Duncan Tulimieri

## Slide 2: Introduction
Proprioception
  Position Sense – static
  Kinesthesia – dynamic
Frequently impaired after stroke
Clinical assessments of proprioception
  Passive movement direction discrimination (PMDD)
    Measure kinesthesia
    Joint is passively flexed/extended, subject report perceived direction
  Matching
    Measure position sense
    Therapist move joint of one side passively, patient mirror match perceived location of joint

## Slide 3: Introduction
Clinical measures
  Subjective
  Poorly standardized
  Too coarse to detect subtle changes
  No control for muscle thixotropy
  Confounds with pain, spasticity, or motor deficit
  Sensitivity and bias of perception not distinguishable
    Sensitivity – inverse of spread of measurements of proprioception
    Bias – mean of errors
      Independent measures
      If known, tailor rehab accordingly

## Slide 4: Introduction
Clinical tests of position sense involve movement
  True position sense = no movement
Questions:
  Compare 3 methods (PMDD, matching, staircase)
    Test-retest reliability
    Inter-rater reliability
    Best reflect known changes in proprioception with age and skilled movement

## Slide 5: Methods
Subjects
  48 control right-handed
  Seated at table, apparatus at midline
  Elbow at 90˚ and slightly in front of body with forearm on table
  Hand pronated on 25˚ apparatus about 20 cm in front of body
  Index finger 55˚ to subject trunk with other fingers slightly spread

## Slide 6: Methods
Measurement procedures
  Adaptive staircase technique
    Blindfolded
    Remove thixotropy confound
      Press against experimenter and then relax
    Put tablet over hand
    Remove blindfold and instructed to not move hand

## Slide 7: Methods
Measurement procedures
  Adaptive staircase technique
    Line start over tested joint and extended length of the finger
    Report if line to the left or right of finger (2AFC)

## Slide 8: Methods
Measurement procedures
  Adaptive staircase technique
    6 staircases
      Staircase 1 and 2
        Begin 30˚ to the left and right of true position
        10˚ step size
        Switch of report
          Switch direction of line & half step size
        Terminate when reverse 4 times
    Staircase 3-6
      Calculated parameters from first 2 staircases (i.e. bias and sensitivity)
      Center staircases on these estimates rather than true finger position
      Initial step size: 5˚
      Terminate at 4 reversals
  Mean total number of estimates: 58 12

## Slide 9: Methods
Measurement procedures
  Adaptive staircase technique
    P.E.S.T.
      Fit logistic regression to data
      Estimate parameters
        Bias: 50% on psychometric function
        Sensitivity: angular difference between 25% and 75%
    Also analyzed when only running 2 staircase algorithms

## Slide 10: Methods
Measurement procedures
  Adaptive staircase technique

## Slide 11: Methods
Measurement procedures
  Matching
    (Adapted method to typical clinical matching test)
    Blindfolded, both hands on inclined board
      Right – reference
      Left – indicator
    Place fingers on intersecting lines
    Control for thixotropy
    Experimenter move fingers
      Place right at 55˚
    “move left finger to mirror match”
    Record angular deviation
    Repeat 10 times

## Slide 12: Methods
Measurement procedures
  Matching
    Bias = mean of 10 trials
    Sensitivity = standard deviation of 10 trials

## Slide 13: Methods
Measurement procedures
  Passive movement direction discrimination threshold (PMDD)
    (Adapted method to typical clinical matching test)
    Blindfolded, place right hand on board
      Reduce chance of other sensors, tape finger to stick
    Control for thixotropy
    Experimenter move 5˚ L/R
      2 seconds (counted by experimenter)
    Report direction
    Back to center
    Repeat
      3 L, 3 R (random)
      Wrong answer: increase step size 5˚
      Correct answer: half step size

## Slide 14: Methods
Measurement procedures
  Passive movement direction discrimination threshold (PMDD)
    Threshold
      Smallest angle with no mistake
      Biomechanical constraints: [1.25 15]

## Slide 15: Methods
Statistical analysis
  Dependent variables
    Staircase bias and sensitivity, Matching mean and SD, PMDD threshold
  Test-retest
    ICC of 5 dependent variables comparing session 1 to session 2
  Inter-rater reliability
    ICC of 5 dependent variables comparing rater 1 to rater 2
  Construct validity
    Stepwise multiple regression of dependent variables on 3 predictors (age, sport years x hours per week, music years x hours per week
  Correlation between each pair of tests

## Slide 16: Results
20/48 subjects - test-retest
  ~ 2 weeks apart
11/48 subjects – inter-rater
  Same day
  Rate quality of sleep, fatigue from session, and attention during session

## Slide 17: Results
Test-retest reliability (1 (best) – 3 (worst))
  1. Staircase algorithm
    Bias most stable and strongest test-retest
      Evident across age
        Younger – less bias, older – more bias
      Regardless of # of staircase
    Sensitivity consistent, but no age difference
      Lack of spread of data
  2. PMDD
    Learning effect
  3. Matching
    Least stable
Fig. 2
Notes: Young person over their two sessions

## Slide 18: Results
Test-retest reliability (1 (best) – 3 (worst))
  1. Staircase algorithm
    Bias most stable and strongest test-retest
      Evident across age
        Younger – less bias, older – more bias
      Regardless of # of staircase
    Sensitivity consistent, but no age difference
      Lack of spread of data
  2. PMDD
    Learning effect
  3. Matching
    Least stable
Fig. 3
Notes: Old person over two sessions

## Slide 19: Results
Fig. 4
Notes: Test-retest

## Slide 20: Results
Inter-rater reliability (1 (best) – 3 (worst))
  Bias
    1. Staircase algorithm
      Regardless of # of staircases
    2. Matching
    3. PMDD
  Sensitivity
    1. Matching
    2. Staircase algorithm
      Lack of spread
    3. PMDD

## Slide 21: Results
Notes: Inter-rater reliability (1 (best) – 3 (worst)
  Bias
    1. Staircase algorithm
      Regardless of # of staircases
      Variance – lack of spread
    2. Matching
    3. PMD
  Sensitivity
    1. Matching
    2. Staircase algorithm
      Lack of spread
    3. PMDD

## Slide 22: Results
Construct validity
  Age only significant predictor (staircase algorithm)
    Strongly predict bias
    Not for sensitivity
  Age only significant predictor (PMDD)
    Threshold
  None (matching)

## Slide 23: Results
Construct validity
  Staircase algorithm bias and PMDD threshold tended to be correlated
  Staircase algorithm sensitivity and matching SD tended to be correlated

## Slide 24: Discussion
Strengths and limitations of the techniques

## Slide 25: Discussion
Strengths and limitations of the techniques

## Slide 26: Discussion
Strengths and limitations of the techniques

## Slide 27: Discussion
Strengths and limitations of the techniques

## Slide 28: Discussion
Strengths and limitations of the techniques

## Slide 29: Discussion
Strengths and limitations of the techniques

## Slide 30: Discussion
Strengths and limitations of the techniques

## Slide 31: Discussion
Strengths and limitations of the techniques
  Adaptive staircase method
    6 staircases (5-6 minutes)
    2 staircases (2-3 minutes)
    No movement
    Parse out specific damage (bias or sensitivity)
  Matching
    Can’t tell which side is impaired
    Cheat by just relaxing
    Motor deficits play a role
  PMDD
    Magnitude and speed of movement poorly controlled
    Subject gain information from movement back to center
    Long time to get accurate estimate

## Slide 32: Discussion
Other considerations
  Bias vs. sensitivity in static position sense measurement
    Bias was important in analyses, sensitivity not so much
      Probably because of sample

## Slide 33: Discussion
Other considerations
  Skilled movement and comparison across methods
    Age only had a significant role
      Probably sample

## Slide 34: Conclusions
Better (accurate & reliable) & feasible test for static proprioception of MCP joint for the clinic
  Can be improved
    Improved algorithm
    Other joint angles