## Slide 1: Robotic Identification of Kinesthetic Deficits After Stroke
Semrau et al., 2013
Duncan Tulimieri

## Slide 2: Introduction
Proprioception
  Position sense – static
  Kinesthesia – dynamic
Proprioception impaired in ~50-60% individuals after stroke
Clinical tools (poor)
Robots provide a promising approach
  Accuracy, precision, continuous

## Slide 3: Introduction
~50 % of individuals post-stroke have position sense deficits
?? % of individuals post-stroke have kinesthetic deficits
  Hard to quantify using current tools
Hypothesis: stroke may result in significant kinesthetic deficits that can be reliably quantified using robotic technology

## Slide 4: Methods
Subjects
  Inclusion (stroke):
    First onset, clinically diagnosed unilateral stroke, understand task instructions
  Exclusion (stroke):
    Visuospatial neglect, significant active medical issues (angina, uncontrolled hypertension, respiratory distress), bilateral stroke, other neurological diagnoses, significant upper body injuries

## Slide 5: Methods
Clinical Assessments
  Edinburgh Handedness Inventory
  Chedoke-McMaster Stroke Assessment Impaired Inventory for Arm and Hand
  Purdue Peg Board
  Thumb Localizing Test
  Behavioral Inattention Test
  Functional Independence Measure
  No significant difference between differences for left and right affected individuals

## Slide 6: Methods
Kinesthesia Task
  KINARM exoskeleton
  Robot move arm (ATBA) to 1 of 3 locations
  Subject see target and hand position, move to target (nATBA)
  * Trial start *
  Hand cursors extinguished
  Random time interval (1500+/- 250 ms)
  Robot move arm (ATBA) to 1 of 2 locations @ 0.28 m/s
    20 cm
  As soon as feel movement, mirror match to best of their ability with (nATBA)

## Slide 7: Methods
Kinesthesia Task
  Control subjects perform with both arms
  Stroke – robot move more affected, mirror match with less affected
  36 total movements
  Move within 10s of ATBA movement
    Non-movement trial

## Slide 8: Methods
Kinesthesia Task
Notes: Need MATLAB
Need to VPN
Open through downloads folder
  Maybe need matlab

## Slide 9: Methods
Kinesthesia Task

## Slide 10: Methods
Kinesthesia Task

## Slide 11: Methods
Kinesthesia Task

## Slide 12: Methods
Kinesthesia Task

## Slide 13: Methods
Kinesthesia Task

## Slide 14: Methods
Data Analysis
  Mirror transpose x-direction of active (nATBA) arm to compare between 2 limbs
  Minor differences in peak speeds (+/- 0.028 m/s) and distance (+/- 0.016 cm)

## Slide 15: Methods
Data Analysis
  Response latency (RL):
      Movement onset = time when 10% maximum speed of movement

## Slide 16: Methods
Data Analysis
  Peak Speed Ratio (PSR):
      1 = perfect match
      < 1: active (nATBA) slower
      > 1: active (nATBA) faster

## Slide 17: Methods
Data Analysis
  Initial Direction Error (IDE):
    Absolute angular deviation of hands at peak speeds

## Slide 18: Methods
Data Analysis
  Path Length Ratio (PLR):
      Ability to match distance of hand movement
      Movement end = time when 10% maximum speed of movement (after peak)

## Slide 19: Methods
Variability
  Standard deviation of all movements
  Add suffix “v”

## Slide 20: Methods
Statistical Analyses
  Calculate 95% confidence intervals for control subject's metrics
    1-sided (IDE, RL) [0% – 95%]
    2-sided (PLR, PSR) [ 2.5% - 97.5%]
  Those outside 95% CI were significantly different from control
  Linear regression to compare robotic and clinical
    Bonferroni corrections for multiple comparisons

## Slide 21: Results
Subjects
  74 control
  113 subject with stroke
  Control
    95% <= 1 non-movement
  LA
    42% >= 1 non-movement
    15% failed to move in >25% of trials
  RA
    29% >= 1 non-movement
    14% failed to move in > 25% of trials

## Slide 22: Results
Response Latency
  Mean
    47% LA outside normative range
    20% RA outside normative range
  Variability
    42% LA outside normative range
    22% RA outside normative range

## Slide 23: Results

## Slide 24: Results

## Slide 25: Results
Peak Speed Ratio
  Mean
    32% LA outside normative range
    27% RA outside normative range
  Variability
    44% LA outside normative range
    39% RA outside normative range

## Slide 26: Results
Initial Direction Error
  Mean
    69% LA outside normative range
    49% RA outside normative range
  Variability
    55% LA outside normative range
    26% RA outside normative range

## Slide 27: Results

## Slide 28: Results

## Slide 29: Results
Path Length Ratio
  Mean
    42% LA outside normative range
    31% RA outside normative range
  Variability
    56% LA outside normative range
    37% RA outside normative range

## Slide 30: Results
Parameter Summary
  5% control outside normative range for > 2 parameters
  71% LA & 49% RA outside normative range for >= 3 parameters

## Slide 31: Results
Clinical and Anatomic Significance
  Nearly all parameters significantly correlated with FIM and FIM motor sub-score
  IDE and IDEv significant predictor of poor performance on all clinical measures evaluated
  Subjects that failed kinesthesia performed significantly worse on clinical tests
  Significantly impaired kinesthesia in 76% of right MCA and 49% left MCA

## Slide 32: Discussion
Robotic Quantification of Kinesthesia
  Position matching paradigm
    Ipsilesional deficits
    Impaired interhemespheric transfer

## Slide 33: Discussion
Relationship of Robotic Measures to Clinical Scores
  Kinesthetic impaired could contribute to poor clinical score
  Significantly related to: FIM, CMSA
    IDE (LA and RA) and IDEv (LA) related to nearly all clinical measures
  Correlations most likely due to contribution of significant sensory deficit to the overall level of functional impairment seen in individuals with stroke

## Slide 34: Discussion
Differences in LA and RA Strokes
  Clinical measures
    No significant difference between severity of stroke between 2 groups in:
      FIM, CMSA, and PPB
  Robot measures
    17% more LA subjects impaired compared to RA
      Right hemisphere dominance for kinesthetic information
        Lateralization ?

## Slide 35: Discussion
Clinical Use of Measuring Kinesthetic Deficits
  61% of those with stroke had significant deficits in kinesthesia
  Clinical measures have difficulty differentiating between motor and sensory deficits
  How to train kinesthesia ?

## Slide 36: Conclusion / Next Steps
What about position sense for these same people?
What about more speeds than just 0.28 m/s?
What about more directions than just 3?
What about more distances than just 20 cm?